## Slide 1: FPGA Hero
Guitar Hero in VHDL

## Slide 2: Overview
Introduction
  Project introduction
  System introduction
SOPC
Graphics
Guitar
Music

## Slide 3: Why?
Show the power of fast prototyping in SOPC
A project with a lot of technological posibilities
Use VHDL for a non traditional purpose

## Slide 4: Who?
Engineering College of Aarhus
  Paul Martin Bendixen
  Morten Stigaard Laursen
  Henrik Hagen Rasmussen
  Kim Arild Steen

## Slide 5: How?
SOPC for the system layout (NIOS II, Avalon bus etc.)
Selfmade VHDL components
IP’s for the remaining components

## Slide 6: What?
Decoding of MIDI files
Interfacing with PS2 guitar controller
Interfacing with VGA
Communication via the Avalon bus
Interfacing with audio codec and SD card
NIOS II

## Slide 7: System Components
VGA
Audio
MIDI decoding
Controller interface
SD Card
Filesystem
Gameplay
  Score update
  Hit or miss a node

## Slide 8: VGA and Gameplay
25MHz pixel Clk
Strict timing requirements
Few states
Ideal for HDL implementation

## Slide 9: Audio
Timing requirements (I2S bus)
More complex initialization (I2C bus)
High complexity for init, low complexity for run mode
Can be split in HDL and software
HDL part taken from Demonstration example

## Slide 10: Controller interface
Short pulses
Low bandwith
Few states
Chose HDL, instead of IRQ

## Slide 11: SD Card
Fast clk (up to 50MHz)
Loose timing requirements
To get a high throughput HDL is a must
We chose software because of existing library (Demonstration system for DE1 board)

## Slide 12: Filesystem
Using existing GPL library called DOSFS

## Slide 13
SOPC Overview

## Slide 14: Software Overview

## Slide 15: The real Guitar Hero Graphics
Notes: <number>

## Slide 16: Our simplification
Simple graphics
  Square notes
  No background
  No perspective
  Hit and miss are shown by changing the color
    White for hit
    Magenta for miss
Notes: <number>

## Slide 17: Output
Format: VGA
Resolution: 640 x 480
Frame rate: 60 Hz
Connected to 4 bit DAC.
Notes: <number>

## Slide 18: Properties of VGA
Pixel order
Blanking
Synchronization
Pixel frequency
Notes: <number>

## Slide 19: VGA timing
Notes: <number>

## Slide 20: Hit, miss and score
Hit and miss detection
  Build in to Graphical part
Score
  IP: CharROM
  Showing Hex score
Notes: <number>

## Slide 21: Score
IP: CharROM
Showing Hex score
Notes: <number>

## Slide 22: VGA Interface
Output
  4 bit DAC resister network for R, G and B
  Hsync
  Vsync
Input
  Avalon
Notes: <number>

## Slide 23: Input interface
Avalon
Notes: <number>

## Slide 24: Guitar Interface

## Slide 25: SPI
Standard SPI
Extensions
  ACKnowledge

## Slide 26: Command communication
Polls via SPI
Recieves Actual button presses
Is able to send 8 bit data

## Slide 27: Changing Modes
Guitar will not work in standard mode
Change to Analog mode
Sending several commands

## Slide 28: Decoding MIDI files
Contains info about the music
Only guitar notes are used
Thanks to the ”Frets on fire” project

## Slide 29: Questions / Frågan

## Slide 30: Demo