## Slide 1
Nintendo Entertainment System on a chip
-
Patrik Eliardsson
Per Karlström
Richard Eklycke
Ulrika Uppman

## Slide 2: Agenda
About NES
Hardware Overview
Video
  Picture Processing Unit (PPU)
  VGA Output
Sound
  Audio Processing Unit (APU)
  Sound Controller
CPU
Testning
Performance
Final words

## Slide 3: Background of the Project
Nintendo Entertainment System (NES)
  A video game console
  Entered the market in 1983, 15 July
  Widely popular
  Over 700 game titles released
Project Goal
  Creating a NES on an FPGA
  Use orginal games and controlls
  Develop our hardware development skills
Notes: Is there someone in here who does not know what the NES is?

## Slide 4: System Overview
Notes: Fixme

## Slide 5: Difficulties Designing a NES
Different clocks for each subsystem
Communication between the subsystems
No official documentation
Most documents are for/by software emulator implementors, no hardware ”thinking”

## Slide 6: Video Subsystems
Picture Processing Unit (PPU)
  Introduction of Video RAM (VRAM)
  Overview of the PPU
  Playfield / Background
  Sprites
  Interfacing with the PPU
VGA Output
  Buffering of the video signal
  Pixel sizing

## Slide 7: Picture Processing Unit (PPU) - VRAM Introduction
Pattern Tables (tiles for background and sprite)
  16 bytes for each tile
  256 tiles
Name Tables (index pointer to pattern table)
  32x30 gives a resultion of 256x240
Attribute tables (1 for each NT, color key for 2x2 tile)
Color Palettes (1 for background, 1 for sprites)
  13 colours, keyed by 2 bits from Attribute table and 2 bit from Pattern table
  X X X X
Attribute table bits
Pattern table bits
Notes: two pattern tables at $0000 and $1000
least significant two bits of the 4-bit
Matrix of tile index

## Slide 8: Picture Processing Unit (PPU) - VRAM Introduction
Sprites
  256 byte sprite memory
  4 byte / sprite, gives 64 sprites
    Y-coordinate
    Pattern table index
    Attribute bits (horizontal flipp, vertical flip)
    X-coordinate

## Slide 9: PPU – System Overview

## Slide 10: PPU – Scanline Details

## Slide 11: PPU – Frame Details

## Slide 12: PPU – Fetch Background Tiles
Notes: 4 mem accesses -> 8 clock cycles
8 clock cycles to fecth 8 pixels
Have to output a pixel every clock cycle
Shift registers.
Fecth byte from NT -> index to PT
Fetch byte from AT -> select 2 bits
Fetch first byte from PT -> store it in upper part
Fetch second byte from PT -> store it in upper part
Repeted 32 times to output 256 pixels

## Slide 13: PPU - Registers
$2000 Control Register 1 (W)
$2001 Control Register 2 (Mask Register) (W)
$2002 Status Register (R)
$2003 SPR-RAM Address Register (W)
$2004 SPR-RAM Data Register (RW)
$2005 PPU Background Scrolling Offset (W2)
$2006 VRAM Address Register (W2)
$2007 VRAM Read/Write Data Register (RW)
Notes: Asynchronous reads by CPU using a higher speed clock on reg controller
VRAM synchronized on PPU clock

## Slide 14: VGA
Buffering of PPU output data
  Using SRAM
  Continuous reading and writing
  Different read/write speed
  SRAM controller
Output to monitor
  from 256x240 to 640x480
  Read line twice
  5 cycles per pixel in 50 MHz
  ”Stretched” pixels
Notes: buffering:
- different output speed from ppu and to vga
PPU pixel output speed: appr 5,3 MHz
VGA output speed: 25 MHz
5 cycles per pixel in 50 MHz => 2,5*256 = 640 in 25 MHz
stretched pixels in original NES
square pixels easy to implement
- black edges
- 4 clk per pixel
different interpolation algorithms

## Slide 15: Sound
Audio Processing Unit
  Background
  Overview
  Sample of subsystem – Square channel
  Interface
Sound Controller
  Background
  Overview
  Configuration

## Slide 16: Audio Processing Unit (APU) - Introduction
5 channels
  2 square channels
  1 triangle channel
  1 noise channel
  1 delta modulation channel
Status register

## Slide 17: Audio Processing Unit (APU) - System Overview

## Slide 18: Audio Processing Unit (APU) - Square Channel
Envelope
Sweep
Timer/2
Sequencer
Length
DAC

## Slide 19: Audio Processing Unit (APU) - Mixer
Some mathematical formulas involving division and addition

## Slide 20: Audio Processing Unit (APU) - Mixer
Some mathematical formulas involving division and addition

## Slide 21: Audio Processing Unit (APU) - Controlling the Channels
$4000 | ddle nnnn | Waveform shape
$4001 | eppp nsss | Frequency sweep
$4002 | pppp pppp | Timer period
$4003 | llll lppp | Length index and timer period

## Slide 22: Sound Controller
APU
8
CODEC
FPGA
BOARD
AUDIO
CTRL
I2C
CONF
SEND
DATA
24 (s)
i2c

## Slide 23: 6502 CPU
Background
Implementation
Memory map of the system
Writing software

## Slide 24: 6502 CPU - Background
Released in 1975
A modified 6502 called 2A03 used in the NES
8-bit data bus, 16-bit address bus
1 accumulator register (A), 2 index register (X, Y)
2 interrupts
  Non-maskable interrupt (NMI)
  Interrupt Request (IRQ)

## Slide 25: 6502 CPU - Implementation
For now, we use a free implementation of the 6502
  Free6502
  Thank you!
Timing problems with Free6502
  Some intructions take too many cycles to execute
Own rewrite of the 6502

## Slide 26: 6502 CPU - Memory Map
Address Range | Size | Notes (Page size is 256 bytes)
$0000 - $00FF | 256 bytes | Zero Page
$0100 - $01FF | 256 bytes | Stack memory
$0200 - $07FF | 1536 bytes | RAM
$0800 - $0FFF | 2048 bytes | Mirror of $0000-$07FF
$1000 - $17FF | 2048 bytes | Mirror of $0000-$07FF
$1800 - $1FFF | 2048 bytes | Mirror of $0000-$07FF
$2000 - $2007 | 8 bytes | Input / Output registers (PPU)
$2008 - $3FFF | 8184 bytes | Mirror of $2000-$2007 (mulitple times)
$4000 - $401F | 32 bytes | Input / Output registers (APU, Controllers)
$4020 - $5FFF | 8160 bytes | Expansion ROM
$6000 - $7FFF | 8192 bytes | Save RAM
$8000 - $BFFF | 16384 bytes | PRG-ROM lower bank - executable code
$C000 - $FFFF | 16384 bytes | PRG-ROM upper bank - executable code
$FFFA - $FFFB | 2 bytes | NMI Handler address
$FFFC - $FFFD | 2 bytes | Power on reset handler routine address
$FFFE - $FFFF | 2 bytes | Software interrupt handler routine address

## Slide 27: Performance
A complete NES including PPU, APU, CPU
DAC interface
VGA interface
SRAM interface
Program and video pattern ROMs for demonstration
Memory usage: 207031 bits (86%) (... bits for demo ROMs)
Logic usage: 3681 LE (20%)

## Slide 28: Final Words
Future for the project
  Integrate cartridge
  Support hand controllers
  HQ2X graphic filter
  Develop our own set of games!
  Save screen or game state
We would like to thank:
  Altera
  The Department of Electrical Engineering, Linköping University
Notes:   Save screen: maybe even possible to save game screen as jpeg by using the nios to convert the image

## Slide 29: Questions?
www.liu.se